FINAL PUBLISHABLE SUMMARY REPORT

Irrigation of the root canal with antibacterial solutions is indispensable during root canal treatment in order to remove biofilm, tissue remnants and dentin debris from the root canal. Nonetheless, still 50% of the root canal treatments fail as a consequence of poor cleaning. Ultrasonic activation of the irrigant has been shown to dramatically increase cleaning efficiency.

During the past 2 years Dr. Christos Boutsioukis worked in the Physics of Fluids group at the University of Twente under a Marie Curie Intra- European Fellowship, to develop a numerical model of Ultrasonically Activated Irrigation in 2-D and 3-D. The model was validated against experimental data acquired by high-speed imaging. Subsequently, it was applied to study the effect of various parameters, such as the shape and position of the ultrasonic file, and the size of the root canal, in an attempt to obtain valuable information about this method and optimize its cleaning efficiency.

The findings of this project may result into the improvement of the success rate of endodontic treatment. Dentists could be motivated to apply ultrasonic activation of the irrigant and dental schools could incorporate this method in the undergraduate and postgraduate curriculum. Companies engaged in the production of dental ultrasonic equipment could use the findings of this project to improve their products and clarify the indications and contra-indications for their use. Researchers can use the developed model to study additional parameters involved in ultrasonic activation of the irrigant.

During this project the participant was trained in the development of numerical models involving Fluid-Structure interaction and two-phase flow. In addition, he was also trained in the application of high-speed imaging and Particle Image Velocimetry techniques, in high-speed electronic sampling techniques and in the use of conductivity probes to measure electrolyte concentration. At the same time, co-supervision of several research projects within the fields of Dentistry and Fluid Dynamics provided important experience for future projects.

Contact details:

Prof. M Versluis

Physics of Fluids, University of Twente, The Netherlands.

+31 53 489 6824

m.versluis@utwente.nl

Dr. C. Boutsioukis

Department of Endodontology, Academic Center for Dentistry Amsterdam (ACTA),

The Netherlands.

+31 20 598 0140

c.boutsioukis@acta.nl

Scientific publications

- Verhaagen B, Boutsioukis C, Heijnen GL, van der Sluis L, Versluis M. Role of the confinement of a root canal on jet impingement during endodontic irrigation. Experiments in Fluids 2012;53:1841-53.

- Verhaagen B, Boutsioukis C, van der Sluis L, Versluis M. Acoustic streaming induced by an ultrasonically oscillating endodontic file. Submitted to Journal of the Acoustical Society of America.

- Boutsioukis C, Verhaagen B, Walmsley AD, Versluis M, van der Sluis LWM. Measurement and visualization of file-to-wall contact during Ultrasonically Activated Irrigation in vitro. International Endodontic Journal 2013; In press (DOI: 10.1111/iej.12097)

- Boutsioukis C, Psimma Z, Kastrinakis E. The effect of flow rate and activation on irrigant extrusion ex vivo. Submitted to International Endodontic Journal.

- Boutsioukis C, Kastrinakis E, Lambrianidis T, Verhaagen B, Versluis M, van der Sluis LWM. Formation and removal of apical vapor lock during syringe irrigation: a combined experimental and Computational Fluid Dynamics approach. International Endodontic Journal 2013  In press (DOI: 10.1111/iej.12133).

- Verhaagen B, Boutsioukis C, Sleutel CP, Kastrinakis E, van der Sluis L, Versluis M. Irrigant transport into dental microchannels. Submitted to Microfluidics and Nanofluidics.

- Boutsioukis C, Psimma Z, van der Sluis LWM. Factors affecting irrigant extrusion during root canal irrigation: a systematic review. International Endodontic Journal  2013;46:599–618.

- Psimma Z, Boutsioukis C, Vasiliadis L, Kastrinakis E. A new method for real-time quantification of irrigant extrusion during root canal irrigation ex vivo. International Endodontic Journal  2013;46:619–631.

- Psimma Z, Boutsioukis C, Kastrinakis E, Vasiliadis L. The effect of needle insertion depth and root canal curvature on irrigant extrusion ex vivo. Journal of Endodontics 2013;39:521-4.

- Boutsioukis C, Kishen A. Fluid dynamics of syringe-based irrigation to optimise anti-biofilm efficacy in root-canal disinfection. Roots 2012;8:22-31.

- Boutsioukis C. The effect of instrumentation on root canal disinfection. Endodontologia 2010;5:117-25.